## Slide 1: L2_1 Bayesian framework for uncertainty analysis
Gürkan Sin, Associate Professor
PROSYS- DTU Chemical Engineering

## Slide 2: Agenda
9:00-12:00 | L2.1 Bayesian framework for parameter estimation
 | Exercises
Lunch break | 
1:00-4:00 | L2.2 Monte Carlo procedure
 | Exercises

## Slide 3: Objective of this lecture
At the end of the lecture, you should be able to:
  Understand and apply in a generic sense bayesian inference to the parameter estimation and uncertainty problem for nonlinear models
  Understand basic concept of numerical methods for Bayesian inference : in particular mcmc (markov-chain monte carlo) sampling methods such as metropolis algorithm, metropolis-hasting, adaptive metropolis, etc …
  Calculate & interpret joint posterior probability density of model parameters as well as make inferences about the uncertainty of model outputs from mcmc simulations (including mean, variance,…)

## Slide 4: Outline
Bayesian theorem
Bayesian analysis for nonlinear regression
Numerical methods for solving Bayesian PE problems
Example 1: Bivariate distribution function
Example 2: Monod model
Exercise: OUR model
Recap
Copyright notice related to Matlab scripts

## Slide 5: Bayesian inference
Unlike other statistical inference methods such as Frequentists, Bayesian statistics treats parameters, θ, and, model variables, ymodel, as variables described by probability statements
The probability statements are conditioned on the measurements, y :
Probability notation:
The terms ’distribution’ and ’density’ are used interchangeably.
Standard distributions are identified with their names. E.g. if θ has a normal distribution with mean, μ and variance, σ2, one writes this as follows:

## Slide 6: Bayesian theorem
Bayes’ rule provides a mathematical framework to update your beliefs (prior information) about a variable, θ , given observations, y. Mathematically, Bayes’ rule calculates the posterior probability of θ given observations, p(θ|y), as follows:
Where is also called a normalizing constant that make sure the sum of integral of posterior density is equal to 1. An equivalent form of this rule is the following which yields unnormalized posterior density:
This summarizes the technical core of Bayesian inference. The primary task of any application is to develop a model and make necessary computations for p(θ|y)
posterior
prior
likelihood
(normalizing) constant

## Slide 7: Bayesian inference for predictive distributions
Given the observations y and the model p(y|θ), predictive distribution of y*, p(y*|y), can be calculated once the posterior probability , p(θ|y), is obtained as follows:
In simple words, future prediction are calculated using the updated probability of p(θ|y) similar to making a prediction for y* using single value of θ in traditional sense.
This integral is caculated using monte carlo simulation strategies such as markov-chain monte-carlo algorithms.

## Slide 8: Numerical methods for bayesian inference
The functions involved in bayesian theorem (likelihood , the integral of normalizing constant) are higher dimensional functions for which analytical solutions rarely exist. Instead simulation methods known as sampling are used .
Some simulations methods are:
Rejection sampling
Importance sampling
Gibbs sampling
Markov Chain Monte Carlo (MCMC) simulation

## Slide 9: Markov chain simulation –in brief
Markov chain simulation draw samples from a target distribution, π(θ), which after a sequence of iteration (simulations) will converge to posterior distribution,p(θ|y).
By definition, Markov chain is a sequence of random variables θ1 ,θ2, θ3,… for which, for any k, the distribution of θk depends only on the most recent one, θk-1.
In practice, several independent sequences of Markov chain simulation are created:
θ k k=1,2,3… by starting at some point θ0, and then for each k a sample, θk , is drawn from a transition distribution T(θk| θ k-1) which depends on previous value.
Many sampling methods have been developed for sampling from transition distributions and are still being developed (active research area). We will look at metropolis and metropolis-hasting algorithms developed early on giving birth to this field.

## Slide 10: Metropolis algorithm
The metropolis algorithm is an adaptation of a random walk that uses an acceptance/rejection rule to converge to the specified target distribution. The algorithm proceeds as follows:
Step 1: select initial parameter vector, θ0
Step 2: iterate as follows for k=1,2,3…
  Create a new trial position, θ*= θk-1+ Δθ
  where Δθ is randomly sampled from jumping distribution q(Δθ)
  Calculate metropolis ratio
  Accept new sample if:
Note this requires jumping distribution to be symmetric: q(θ*, θk-1)= q(θk-1, θ*)

## Slide 11: Metropolis-hasting algorithm
The metropolis-hasting algorithm is a generalisation of metropolis algorithm in which jumping distribution need not be symmetric and the acceptance/rejection rule is updated as follows:
The rest remains the same.

## Slide 12: Simple example: bivariate unit normal distribution
To illustrate the metropolis algorithm (mcmc in general for that matter), we will use bivariate unit normal density function.
the task is to use mcmc sampling to converge to the target density function.
Target density is bivariate unit normal: π(θ|y)=N(θ|0,C) where C is 2x2 identity matrix
Jumping distribution also bivariate normal centered at current iteration and scaled to 1/5 the size: q(θ*| θk-1)= N(θ*|θk-1,0.22C)
Matlab implementation of metropolis algorithm also known as random walk algorithm

## Slide 13: Metropolis algorithm in Matlab
%%step 1 draw a starting point for each chain.
mu = [0 0]; % C = eye(2); % C is identity matrix R = chol(C); npar=length(mu); covscale=2.4 / sqrt(npar); % important.
x0= mvnrnd(mu,C,chainnumber) ; %bivariate normal
%step 2: perform sampling
for j=1:chainnumber
x=x0(j,:);
for i=1:samplingnumber
%2.1 sample a proposal from jumping distribution
u = randn(1,npar); % draw a random number
dx=u*R*covscale; % incremental walk
xp=x+u*R*covscale; % new trial position
%2.2 calculate the metropolis ratio:
r= mvnpdf(xp,mu,C) ./ mvnpdf(x,mu,C); ratio(i,:)=r';
%2.3 reject/accept new sample
if min(r,1) > random('unif',0,1) % probability min(r,1)
x=xp ; else x=x;
end
end

## Slide 14: Simple example: bivariate normal density
Random walk
(5000 mcmc steps)
the impact of initial point
(prior knowledge).
It is quickly updated (bayesian)
With new information.
That is the reason why we use burn in ratio.
i.e. omit first 20 or 50% of data in postprocessing

## Slide 15: Simple example: bivariate normal density
5 chains and 50 simulations: random walk starting from different points
5 chains and 1000 simulations: random walk is hidden
The scaling factor used for jumping distribution is an important property. It was purposely chosen as 0.2 to make the jumping inefficient to see the random walk aspect in the figure-left. For a better performance, suggested efficiency scaling ~ 2.4/sqrt(d) where d is the dimension of the target distribution function (Gelman et al. 2004).

## Slide 16: Simple example: bivariate normal density scaling factor versus acceptance ratio
5 chains and 1000 simulations:
Scale = 1.2 vs AR=0.48
5000 simulations:
scale 2.4/sqrt(d) v s AR=0.35
Optimal acceptance ratio (AR) is 0.44 for d=1 and decreases to 0.23 for d>5 (Gelman et al 2004)

## Slide 17: Compare the accepted versus rejected samples
Random walk metropolis algorithm is simple and beautiful, i.e. it works.

## Slide 18: Adaptive metropolis algorithm
we update the covariance matrix based on previous accepted samples.
function [x px R] =am(prior,pdf,T,d)
q =@(C,d) mvnrnd(zeros(1,d),C); % dvariate normal proposal distri
sd=2.38/sqrt(d); % covariance scale
C=sd^2*eye(d); % scaled covariance matrix for proposal distribution
x=nan(T,d); px=nan(T,1); %preallocate memory
x(1,:)=prior(1,d); % initialize chain by sampling from prior
px(1)=pdf(x(1,:)); % compute density of initial state chain
R=[]; % initialize rejected samples
for t=2:T
if mod(t,10)==0 % update covariance matrix every 10th iteration
C=sd^2*(cov(x(1:t-1,:))+1e-4*eye(d)); % update the covariance
end
xp=x(t-1,:)+q(C,d); % generate proposal
pxp=pdf(xp); % calculate density of hte proposal
pac=min(1,pxp/px(t-1)) ; % compute probability of acceptance
if pac>rand % pacc larger than U(0, 1)?
x(t,:)=xp; px(t)=pxp; % true: accept the proposal
else
x(t,:)=x(t-1,:); px(t)=px(t-1);
R=[R;xp]; % store rejected samples
end
end

## Slide 19: Bayesian inference for nonlinear regression
Let us start with definition of regression model, f, and data,y, with independent gaussian errors, e, with some unknown variance, s2,:
is a vector that refer to unknown model parameters, and assumed to have multivariate normal distribution as prior distribution:
The inverse of variance of the residuals typically assumed to follow gamma distribution which approximates gaussian error models (see Gelman et al., 2004):
n0 is the degrees of freedom and s02 is the sample variance. Note that chi-sq is a special case of gamma distribution:

## Slide 20: Bayesian inference for nonlinear regression – Monod example
Let us start with definition of Monod model f, which describes substrate limited microbial growth kinetics, where m is the growth rate (h-1), mmax, is the maximum growth rate (h-1) and Ks affinity coefficient (mgCOD/L):
The parameter estimation problem is the following: given a set of measured growth rates,y, under the following substrate conditions ,S, estimate the unknown mmax, and Ks :
S = [28 55 83 110 138 225 375]; % (mg / L COD)
y= [0.053 0.060 0.112 0.105 0.099 0.122 0.125]; % (h-1)

## Slide 21: Monod example- MCMC implementation
Step 0. Preparatory phase. This step to gain useful information about prior distribution function for the model parameters and to estimate the error variance
Solution: do a quick MLE estimation
% step 0: provide prior information about the unknowns (parameters) and also error function (variance). here we can do an MLE estimation
Ssfun = @(theta,data) sum((data.mu-modelfun(data.s,theta)).^2);
[tmin,ssmin]=fminsearch(ssfun,theta*2,[],data);
n = length(data.mu);
p = length(theta);
s2 = ssmin/(n-p); % estimate the sample variance
J = [data.s./(tmin(2)+data.s), ...
-tmin(1).*data.s./(tmin(2)+data.s).^2];
tcov = s2*inv(J'*J) ; %estimate of the covariance matrix for the priors
tsigma=sqrt(diag(tcov))';
theta=tmin;

## Slide 22: Monod example- MCMC implementation
Step 0: Preliminary results for initilisation of MCMC
Mean estimates | 
mmax | Ks
0.1454 | 49.0529
Covariance: Cov | 
0.000244 | 0.25011
0.25011 | 320.8347
Sample variance,s2=s2
1.6335e-04
MLE estimation
Correlation: Cor | 
1 | 0.8926
0.8926 | 1

## Slide 23: Monod example- MCMC implementation
Step 1. select initial parameter vector, θ0
Multivariate normal distribution is assumed for the parameters using covariance matrix estimated from MLE, C
%%step 1 initialization: draw a starting point for model parameters,define error variance and covariance scale for the jumping distribution
C=tcov;
x0 = mvnrnd(theta,C,chainnumber) ; % sampled from joint multivariate normal distribution using covariance C
sigma2=s2; %error variance as estimated from MLE
npar=length(theta);
covscale=2.4/sqrt(npar); %covariance scale

## Slide 24: Monod example- MCMC implementation
Step 2. do markov chain simulations to sample from target distribution
Recall that the target distribution is a product of prior and likelihood functions.
The likelihood function is defined as follows (prior were as defined previously):
Where
The metropolis ratio becomes then:

## Slide 25: Monod example- MCMC implementation
Step 2. Matlab script of this part of the code
%%step 2: perform mcmc sampling
for j=1:chainnumber
x=x0(j,:);
for i=1:samplingnumber
%2.a sample a proposal from jumping distribution
u = randn(1,npar); %random draw
dx=u*R*covscale; % incremental walk
xnew=x+dx; %new proposal
%2.b calculate the ratio of densities
ssnew=ssfun(xnew,data); sscur=ssfun(x,data);
rm= exp(-0.5*((ssnew-sscur)./sigma2) ); % metropolis ratio
%2.c reject/accept new sample
if min(rm,1) > random('unif',0,1) % probability min(r,1)
x=xnew ;
else
x=x;
end
end

## Slide 26: Monod example- MCMC implementation
Step 2. Results of mcmc sampling using metropolis algorithm what is shown is raw data from simulations using 5 markov chains with 5000 sampling

## Slide 27: Monod example- MCMC implementation
Step 2. Using standard statistically analysis of markov chain simulations provides plentiful information: most importnat is joint posterior distribution for mmax and Ks
Joint posterior distribution
posterior marginal density
Uncertainty characterised entirely all relevant statistics (mean, standard dev, correlation can directly be estimated…

## Slide 28: Monod example posterior simulations
Posterior simulations for the model prediction can be performed by drawing randomly from posterior joint distribution of the model parameters (see previous slide)
%% posterior simulations
% randomly sample from joint posterior distribution
chainb = [y1b y2b]; postsample = 1000;
s=data.s(1):10:data.s(end)+10; % calculate the function at different substrate conc
posttheta = chainb(randi(length(chainb), [postsample 1]),:); % randomly draw from the chain nsample values
ypost=[];
for i=1:postsample
ypost(i,:) = modelfun(s,posttheta(i,:)); % model parameter uncertainty
end
for i=1:length(s)
[fp,xp,flo,fup] = ecdf(ypost(:,i));
x95(i,1)=xp(find(fp<0.95,1,'last')); % Pr(x<X)= 0.95
x05(i,1)=xp(find(fp<0.05,1,'last')); % Pr(x<X)=0.05
end

## Slide 29: Monod example posterior simulations
Posterior simulations with samples drawn randomly from the joint distribution of the model parameters
This concludes the uncertainty analysis of modelling exercise from model parameters to error structure and finally to the predictions of the model….
Mean estimates | 
mmax | Ks
0.1526 | 59.6541
Covariance: Cov | 
0.0003 | 0.3211
0.3211 | 437.7008
Sample variance,s2=s2
1.6335e-04
Bayesian estimation
Correlation: Cor | 
1 | 0.9005
0.9005 | 1

## Slide 31: Monod example posterior simulations – convergence statistics
Convergence statistics via potential scale reduction factor, R
This convergence statistics indicate the potential scale reduction for the current distribution if the sampling were to continue to infinity , i.e. n ∞
  The sampling is said to converge if R is close to 1
Monte carlo error is defined as the error of integration which tends to 0 as n ∞. Hence error on the mean estimate of the distribution is σ/sqrt(n)
convergence achieved & MC error is low!
Convergence statistics |  | 
 | mmax | Ks
R | 1.0132 | 1.0136
MC error | 0.0002 | 0.2715

## Slide 32: Bayesian inference in practice – slowly but surely picking up in engineering community!
Bayesian inference is a thriving area of research thanks to increasing availability of computational power as well as increasing of size and diversity of community (from statistics to engineering in various fields) working on this area
There are some software: BUGS a leading community in this area (both scientifically and software wise).For engineering PE, see the r-project called DREAM: http://dream.r-forge.r-project.org/
Like any other problem solving, when using Bayesain inference, one needs to select the relevant probability models to carry out the analysis. This includes:
  Likelihood function (a probability model)
  Error models (a probability model)
  Prior functions (a probability function)
  Jumping function and covariance scale for the parameters (update necessary or not? Then using adaptive algorithms such as AM)
  Check convergence statistics (especially acceptance ratio and some variance estimation errors see Gelman et al 2004)
In either case, Bayesian inference provides an improved understanding of sources of uncertainty and how they can be approximated. This is quite an added value.

## Slide 33: Exercise: AEROBIC GROWTH OF microorganismS
Uncertainty analysis via Bayesian inference

## Slide 34: Exercise
Please go step by step analysis shown for the Monod example above and apply bayesian inference for the parameter estimation problem in OUR case!
Use the parameter estimation results from lecture 1.2 as a starting point for MCMC sampler. Follow then the steps outlined in slide 10.
The parameter estimation problem was given the OUR example of L1.2. Please check it for the necessary information about data and model to be used.

## Slide 35: Copyright notice of Matlab scripts
Everything contained in this directory and its subdirectories is the property of Department of Chemical and Biochemical Engineering, Technical University of Denmark.
Copyright notice:
The code of these files is free software. Users may modify and redistribute this code. The sole restrictions are that:
In the academic spirit of collaboration, the source code should be appropriately acknowledged in the resulting scientific disseminations. You may cite this code as follows: "Sin G, Lantz AE, Gernaey KV. Good Modeling Practice for PAT Applications: Propagation of Input Uncertainty and Sensitivity Analysis. Biotechnology progress. Biotechnol. Prog., 25: 1043–1053,2009.DOI 10.1021/bp.166."
  (ii) the source code must accompany compiled distributions of this code, and
  (iii) this notice must remain unchanged.
Please report any bugs related to the code to the following email gsi@kt.dtu.dk
Copyright Gürkan Sin DTU Chemical Engineering, Lyngby, DK.

## Slide 36: Solution to OUR exercise setting up Bayesian PE problem
Foremost we choose our probability models for bayesian inference (these are commonly made choices. Other pdf can also be assumed and Bayesian PE can be repeated several times):
  Likelihood function: multivariate normal pdf
  Metropolis ratio:
  Error model: Chisq distribution
  Prior functions: multivariate normal pdf
  Jumping function : gaussian normal pdf
  Covariance scale:

## Slide 37: Solution to OUR exercise
The solution is coded in the folders our exercise3par and our exercise4par
Parameters | Mean | std | Correlation matrix |  |  | 
YSX | 0.4978 | 0.0057 | 1 | 0.847 | -0.2211 | 0.833
μmax | 0.0502 | 0.0007 | 0.847 | 1 | 0.2632 | 0.7049
KS | 0.0232 | 0.0018 | -0.2211 | 0.2632 | 1 | -0.187
kd | 0.0045 | 0.0004 | 0.833 | 0.7049 | -0.187 | 1
MLE
Bayesian
Parameters | Mean | std | Correlation matrix |  |  | 
YSX | 0.4983 | 0.0059 | 1 | 0.8555 | -0.3146 | 0.8456
μmax | 0.0503 | 0.0007 | 0.8555 | 1 | 0.1546 | 0.7351
KS | 0.0236 | 0.0017 | -0.3146 | 0.1546 | 1 | -0.2772
kd | 0.0045 | 0.0004 | 0.8456 | 0.7351 | -0.2772 | 1

## Slide 38: Solution to OUR exercise: MCMC sampling results

## Slide 39: Confidence ellipsoids

## Slide 40: Posterior densities of parameter estimates

## Slide 41: Posterior simulations